ITEM NO.: LS-1239

ASSEMBLY INSTRUCTIONS:

# ※VERY IMPORTANT

PLEASE READ THOROUGHLY. CAREFULLY UNPACK THIS LAMP

AND PLACE ON A SOFT SURFACE.

A.

1. Use screw (2) to tighten the clip (1) into wall/ceiling.

2. Secure the lamp into clip.

3. Use a 28W (maximum) T4 type bulb (bulb included).

4. Connect the cable (3) with lamp (4) as shown, plug in.

B.

1. To connect more pc together, use connector to connect them together.

C、D.

1. For relamping see diagram for removing the T4 Type Bulb and installing

the new bulb.

IMPORTANT SAFETY INSTRUCTIONS:

This portable lamp has a polarized plug (one blade is wider than the other) as

a feature to reduce the risk of electric shock. This plug will fit in a polarized

outlet only one way. If the plug does not fit fully in the outlet, reverse the plug.

If it still does not fit, contact a qualified electrician. Never use with an

extension cord unless plug can be fully inserted. Do not alter the plug.

- PLEASE INFORM YOUR DEALER IMMEDIATELY IN CASE OF ANY

PARTS SHORTAGE.

- SAVE THESE INSTRUCTIONS FOR FUTURE REFERENCE.

# Text boxes

Use 28W (Maximum) T4 Type Bulb. (Bulb included)