ITEM NO.: LS-19682

ASSEMBLY INSTRUCTIONS:

- Determine the height for this fluorescent lamp FITTING, and adjust the wire length.

- Fasten crossbar (1) to junction with screws (2).

- Connect the WHITE WIRE (LIVE) (4) from FITTING to the WIRE (LIVE) from power supply

by using the WIRE NUT (6). Connect the BLACK WIRE (NEUTRAL) (3) to the

WIRE (NEUTRAL) from power supply by using the WIRE NUT (6). Connect the

GROUND WIRE (5) from the canopy (7) to OUTLET BOX, make the electrical

connections by using the WIRE NUT (6).

- Attach the canopy (7) to the crossbar (1) with screws (8).

- Drill the suitable hole in the ceiling and insert the PLASTIC TUBE (9), then

install the HOOK (10) into the PLASTIC TUBE (9).

- Make the steel wire a ring and tighten with WIRE FIXERS (11), then hang up

the fluorescent lamp FITTING to the HOOK (10).

- Push COVER CUP (12) to the right place.

- The steps to replace the FLUORESCENT TUBE: (a1) Pull the LAMP COVER out.

(a2) Turning the FLUORESCENT TUBE then pull them out. (b1) Install the

FLUORESCENT TUBE into the lamp-sockets.(b2) Slide the LAMP COVER on the fluorescent lamp fxiture.

- PLEASE INFORM YOUR DEALER IMMEDIATELY IN CASE OF ANY PARTS SHORTAGE.

- SAVE THESE INSTRUCTIONS FOR FUTURE REFERENCE.

※ THIS LIGHTING FIXTURE CAN NOT BE INSTALLED IN THERMORADIACTIVE ENVIRONMENT.

# Text boxes

Input: 120v ~50/60Hz Watt: 28Wx2

Use 28W (Maximum) T5 Fluorescent tube (Tube included).

FLUORESCENT TUBE