ITEM NO.: LS-19691

ASSEMBLY INSTRUCTIONS:

- Determine the height for this fluorescent lamp FITTING, and adjust the wire length.

- Fasten crossbar (1) to junction with screws (2).

- Connect the WHITE WIRE (LIVE) (4) from FITTING to the WIRE (LIVE) from power supply by using the WIRE NUT (6). Connect the BLACK WIRE (NEUTRAL) (3) to the WIRE (NEUTRAL) from power supply by using the WIRE NUT (6). Connect the GROUND WIRE (5) from the canopy (7) to OUTLET BOX, make the electrical connections by using the WIRE NUT (6).

- Attach the canopy (7) to the crossbar (1) with screws (8).

- The steps to replace the FLUORESCENT TUBE: (a1) Open the PLASTIC COVER from the fluorescent lamp FITTING. (a2) Pull the LAMP COVER out. (a3) Turning the FLUORESCENT TUBE then pull it out. (b1) Install the FLUORESCENT TUBE into the lamp-socket. (b2) Slide the LAMP COVER on the FITTING.(b3) Fasten the PLASTIC COVER to the junction of the fluorescent lamp FIXUTRE.

- PLEASE INFORM YOUR DEALER IMMEDIATELY IN CASE OF ANY PARTS SHORTAGE.

- SAVE THESE INSTRUCTIONS FOR FUTURE REFERENCE.

※ THIS LIGHTING FIXTURE CAN NOT BE INSTALLED IN THERMORADIACTIVE ENVIRONMENT.

# Text boxes

FLUORESCENT

TUBE

Input: 120v ~50/60Hz Watt: 28W

Use 28W (Maximum) T5 Fluorescent tube (Tube included).