ITEM NO.: LS-19692

ASSEMBLY INSTRUCTIONS:

- Determine the height for this fluorescent lamp FITTING, and adjust the wire length.

- Fasten crossbar (1) to junction with screws (2).

- Connect the WHITE WIRE (LIVE) (4) from FITTING to the WIRE (LIVE) from power supply by using the WIRE NUT (6). Connect the BLACK WIRE (NEUTRAL) (3) to the WIRE (NEUTRAL) from power supply by using the WIRE NUT (6). Connect the GROUND WIRE (5) from the canopy (7) to OUTLET BOX, make the electrical connections by using the WIRE NUT (6).

- Attach the canopy (7) to the crossbar (1) with screws (8).

- Drill the suitable hole in the ceiling and insert the PLASTIC TUBE (9), then install the HOOK (10) into the PLASTIC TUBE (9).

- Make the steel wire a ring and tighten with WIRE FIXERS (11), then hang up the fluorescent lamp FITTING to the HOOK (10).

- Push COVER CUP (12) to the right place.

- The steps to replace the FLUORESCENT TUBE: (a1) Open the LAMP COVERS. (a2) Turning the FLUORESCENT TUBE then pull them out. (b1) Install the FLUORESCENT TUBE into the lamp-sockets.(b2) Fasten the LAMP COVERS to junction of the fluorescent lamp FIXUTRE.

- PLEASE INFORM YOUR DEALER IMMEDIATELY IN CASE OF ANY PARTS SHORTAGE.

- SAVE THESE INSTRUCTIONS FOR FUTURE REFERENCE.

※ THIS LIGHTING FIXTURE CAN NOT BE INSTALLED IN THERMORADIACTIVE ENVIRONMENT.

# Text boxes

FLUORESCENT TUBE

Input: 120v ~50/60Hz Watt: 28W X 2

Use 28W (Maximum) T5 Fluorescent tube (Tube included).